## Slide 1
INTRODUCTION TO AEROSPACE ENGINEERING
Stability:
from physics
to a verified feature
Five engineering blocks. Five bounded implementations. One mission decision.
RESTORE
CONTROL
DECIDE
Notes: Open with the payload-moving-aft mission scenario. Do not define stability yet; ask what evidence students would need.
[Sources]
- https://www.faa.gov/regulations_policies/handbooks_manuals/aviation/phak
- https://ntrs.nasa.gov/api/citations/19780017135/downloads/19780017135.pdf
- Local: templates/FEATURE-SPEC.md; examples/stability-unit/README.md
[/Sources]

## Slide 2
CENTRAL TENSION
More stability is not automatically better
02
RESTORING TENDENCY
CONTROL AUTHORITY
MANEUVERABILITY
WORKLOAD + MISSION
A design decision must balance the whole response—not maximize one metric.
Notes: [Sources]
- https://www.faa.gov/regulations_policies/handbooks_manuals/aviation/phak
- https://ntrs.nasa.gov/api/citations/19780017135/downloads/19780017135.pdf
[/Sources]

## Slide 3
LEARNING PROGRESSION
The unit builds one decision across five blocks
03
01
Disturbance, trim, response
02
Longitudinal static stability
03
CG, static margin, loading limits
04
Lateral-directional dynamics
05
Payload moves aft: mission decision
Each block adds a tested capability to the same aircraft model.
Notes: [Sources]
- Local: templates/FEATURE-SPEC.md; examples/stability-unit/README.md
[/Sources]

## Slide 4
ENGINEERING WORKFLOW
The implementation starts before ChatGPT
04
1
QUESTION
2
MODEL
3
BEHAVIOR
4
VERIFY
5
SPECIFY
6
GENERATE
7
DECIDE
AI implements a specification. It does not select the physics or prove the result.
Notes: [Sources]
- Local: templates/FEATURE-SPEC.md; examples/stability-unit/README.md
[/Sources]

## Slide 5
BLOCK 1
Trim is balance; response follows disturbance
05
Trimmed condition
Net pitching moment is zero at the selected condition.
Trim does not mean the aircraft is stable. It only identifies an equilibrium.
Disturbed condition
A gust or control input changes the state.
Static stability asks for the initial tendency. Dynamic stability asks how the motion evolves with time.
Notes: [Sources]
- https://www.faa.gov/regulations_policies/handbooks_manuals/aviation/phak
[/Sources]

## Slide 6
BLOCK 1 PHYSICS
Pitching-moment slope reveals the restoring sign
06
Cm = Cm0 + Cmα α
αtrim = −Cm0 / Cmα
Default case
Cm0 = 0.04
Cmα = −0.8 rad⁻¹
αtrim = 0.050 rad = 2.86°
Chart: Angle of attack
| −2° | 0° | 2.86° | 5° | 8°
Cm | 0.068 | 0.04 | 0 | -0.03 | -0.072
Notes: [Sources]
- https://ntrs.nasa.gov/api/citations/19780017135/downloads/19780017135.pdf
[/Sources]

## Slide 7
BUILD 01
Build a trim-response feature
07
ENGINEERING QUESTION
Is the selected condition trimmed, and does a positive angle-of-attack disturbance create an opposing moment tendency?
Verification before code
• Manual trim-angle calculation
• Positive disturbance changes Cm with the slope sign
• Zero slope produces no restoring tendency
src/student/physics/trim-response.js
src/student/features/trim-response.feature.js
tests/student/trim-response.test.js
Notes: [Sources]
- Local: templates/FEATURE-SPEC.md; examples/stability-unit/README.md
[/Sources]

## Slide 8
BLOCK 2
Static margin locates CG relative to the neutral point
08
SM = (xNP − xCG) / c̄
Positive SM: initial restoring tendency
Zero SM: neutral point and CG coincide
Negative SM: initial divergence tendency
CG
NP
static margin
Moving CG aft reduces the margin.
Notes: [Sources]
- https://ntrs.nasa.gov/api/citations/19780017135/downloads/19780017135.pdf
[/Sources]

## Slide 9
BLOCK 2 VERIFICATION
The reference case predicts a 12.5% static margin
09
xNP = 0.16 m
xCG = 0.12 m
c̄ = 0.32 m
SM = (0.16 − 0.12) / 0.32
SM = 0.125 = 12.5%
Chart: CG location, m
| 0.08 | 0.12 | 0.16 | 0.18
Static margin | 0.25 | 0.125 | 0 | -0.0625
Notes: [Sources]
- https://ntrs.nasa.gov/api/citations/19780017135/downloads/19780017135.pdf
- Local: templates/FEATURE-SPEC.md; examples/stability-unit/README.md
[/Sources]

## Slide 10
BUILD 02
Build a static-margin feature
10
ENGINEERING QUESTION
What longitudinal static margin is implied by the selected CG and neutral point?
Verification before code
• Reference case gives 0.125
• CG at NP gives zero
• Moving CG aft decreases static margin
src/student/physics/static-margin.js
src/student/features/static-margin.feature.js
tests/student/static-margin.test.js
Notes: [Sources]
- Local: templates/FEATURE-SPEC.md; examples/stability-unit/README.md
[/Sources]

## Slide 11
BLOCK 3
Loaded CG is a mass-weighted location
11
xloaded = (mairframe xairframe + mpayload xpayload) / (mairframe + mpayload)
Forward limit
Airframe CG
Loaded CG
Payload
Aft limit
The payload changes total mass and moment about the datum.
Notes: [Sources]
- https://www.faa.gov/regulationspolicies/handbooksmanuals/aviation/phak/chapter-10-weight-and-balance
[/Sources]

## Slide 12
BLOCK 3 VERIFICATION
The loading calculation must agree with two limiting cases
12
Reference calculation
mairframe = 1.35 kg at 0.11 m
mpayload = 0.25 kg at 0.20 m
xloaded = 0.1241 m
Limits: 0.09 m to 0.16 m
Behavioral evidence
Zero payload → loaded CG equals airframe CG
Move payload aft → loaded CG moves aft
CG exactly on a limit → zero limit margin
Notes: [Sources]
- https://www.faa.gov/regulationspolicies/handbooksmanuals/aviation/phak/chapter-10-weight-and-balance
- Local: templates/FEATURE-SPEC.md; examples/stability-unit/README.md
[/Sources]

## Slide 13
BUILD 03
Build a CG-loading feature
13
ENGINEERING QUESTION
Where is the loaded CG, and is it inside the introductory loading limits?
Verification before code
• Reference case gives 0.1241 m
• Zero payload returns airframe CG
• Moving payload aft moves loaded CG aft
src/student/physics/cg-loading.js
src/student/features/cg-loading.feature.js
tests/student/cg-loading.test.js
Notes: [Sources]
- Local: templates/FEATURE-SPEC.md; examples/stability-unit/README.md
[/Sources]

## Slide 14
BLOCK 4
Dynamic stability asks whether motion decays with time
14
Static question
Immediately after a disturbance, is the tendency restoring, neutral, or diverging?
Dynamic question
Does the resulting motion decay, persist, or grow—and how quickly does it oscillate?
A restoring initial tendency does not guarantee an acceptable time response.
Notes: [Sources]
- https://www.faa.gov/regulations_policies/handbooks_manuals/aviation/phak
[/Sources]

## Slide 15
BLOCK 4 PHYSICS
A complex eigenvalue captures decay and oscillation
15
λ = σ ± iωd
ωn = √(σ² + ωd²)
ζ = −σ / ωn
T = 2π / |ωd|
σ < 0 decays σ = 0 persists σ > 0 grows
Chart: Time, s
| 0 | 1 | 2 | 3 | 4 | 5
Amplitude envelope | 1 | 0.549 | 0.301 | 0.165 | 0.091 | 0.05
Notes: [Sources]
- Local: templates/FEATURE-SPEC.md; examples/stability-unit/README.md
[/Sources]

## Slide 16
BLOCK 4 CALCULATION
The default mode decays—but that is not the final decision
16
σ = −0.6 s⁻¹ ωd = 2.4 rad/s
ωn = 2.474 rad/s
ζ = 0.243
T = 2.618 s
Half-amplitude time = 1.155 s
Interpretation still requires context
• Is the response fast enough?
• Is oscillation acceptable?
• What control action is available?
• What workload does the mission allow?
Notes: [Sources]
- Local: templates/FEATURE-SPEC.md; examples/stability-unit/README.md
[/Sources]

## Slide 17
BUILD 04
Build a dynamic-mode feature
17
ENGINEERING QUESTION
Does the supplied oscillatory mode decay or grow, and what are its introductory modal properties?
Verification before code
• Negative σ produces decay
• Positive σ produces growth
• Period follows 2π/|ωd|
src/student/physics/dynamic-mode.js
src/student/features/dynamic-mode.feature.js
tests/student/dynamic-mode.test.js
Notes: [Sources]
- Local: templates/FEATURE-SPEC.md; examples/stability-unit/README.md
[/Sources]

## Slide 18
BLOCK 5 MISSION
The payload moves aft; the stability margin shrinks
18
Initial payload station
0.10 m
Loaded CG 0.1084 m
SM 16.1%
Mission payload station
0.24 m
Loaded CG 0.1303 m
SM 9.3%
The case remains inside the introductory limits—but with less aft margin and less static margin.
Notes: [Sources]
- https://www.faa.gov/regulationspolicies/handbooksmanuals/aviation/phak/chapter-10-weight-and-balance
- https://ntrs.nasa.gov/api/citations/19780017135/downloads/19780017135.pdf
[/Sources]

## Slide 19
ENGINEERING JUDGMENT
A mission decision needs more than a PASS label
19
RESTORING
Is static margin still positive?
CONTROL
Can available control moment trim and maneuver?
LIMITS
How close is loaded CG to the aft boundary?
WORKLOAD
Is the dynamic response acceptable for the operator?
MISSION
Can the payload remain forward or be restrained?
VALIDITY
Where does the simple model stop being trustworthy?
Notes: [Sources]
- https://www.faa.gov/regulationspolicies/handbooksmanuals/aviation/phak/chapter-10-weight-and-balance
- https://www.faa.gov/regulations_policies/handbooks_manuals/aviation/phak
[/Sources]

## Slide 20
BUILD 05
Build a mission-loading feature
20
ENGINEERING QUESTION
After the payload moves aft, do loading limits and positive static margin remain—and what mission decision follows?
Verification before code
• Initial and mission CG calculations
• Aft movement cannot move CG forward
• Decision discusses limits and model validity
src/student/physics/mission-loading.js
src/student/features/mission-loading.feature.js
tests/student/mission-loading.test.js
Notes: [Sources]
- Local: templates/FEATURE-SPEC.md; examples/stability-unit/README.md
[/Sources]

## Slide 21
STUDENT PROCESS
One completed specification is the entire AI request
21
Before ChatGPT
Complete Sections 1–12
Show a manual reference calculation
Define numerical, behavioral, and boundary tests
Name the exact three files
In ordinary ChatGPT
Attach the completed FEATURE-SPEC.md
Ask: “Generate the feature described in this completed specification.”
Save the three complete files exactly where specified
Notes: [Sources]
- Local: templates/FEATURE-SPEC.md; examples/stability-unit/README.md
[/Sources]

## Slide 22
VERIFICATION
Passing tests is evidence—not physical truth
22
SOFTWARE CORRECTNESS
Does the function match known cases?
MODEL CORRECTNESS
Was the intended equation implemented?
MODEL VALIDITY
Do its assumptions fit this condition?
REAL-WORLD VALIDATION
Does evidence agree with reality?
Notes: [Sources]
- Local: templates/FEATURE-SPEC.md; examples/stability-unit/README.md
[/Sources]

## Slide 23
CLOSE
Your final answer must return to the mission
23
The payload moved aft.
What changed?
What evidence do you trust?
What remains uncertain?
What should the operator do?
A feature is complete only when you can explain the physics, defend the tests, and make a qualified engineering decision.
Notes: [Sources]
- https://www.faa.gov/regulationspolicies/handbooksmanuals/aviation/phak/chapter-10-weight-and-balance
- https://ntrs.nasa.gov/api/citations/19780017135/downloads/19780017135.pdf
- Local: templates/FEATURE-SPEC.md; examples/stability-unit/README.md
[/Sources]